## Slide 1: Targeted Mass Spectrometry MRM

## Slide 2: What is MRM?
Multiple reaction monitoring (MRM) is a very sensitive and specific mass spectrometry technique for quantifying chemicals in complicated mixtures. This method use a triple quadrupole MS to target the ion corresponding to the chemical of interest, which is then fragmented to yield a number of daughter ions. Quantitative goals can be achieved by choosing one (or more) of these fragment daughter ions. Within the mass spectrometer, only compounds that match both of these conditions, i.e. particular parent and daughter ions corresponding to the mass of the molecule of interest, are identified. The experiment enhances sensitivity while preserving exceptional accuracy by disregarding all other ions that pass into the mass spectrometer.

## Slide 3
MRM is used to identify particular analytes and quantify proteins, peptides, metabolites, and lipids in plasma, serum, and other biological samples in absolute terms.

## Slide 4: What kind of samples are suitable for analysis?
MRM analysis may be performed on almost any substance that can be ionised and subsequently fragmented. The most common applications include the analysis of proteins and peptides, metabolites, and medicines in complicated mixtures like plasma and serum. The MRM experiment on digested peptides that match to the protein of interest can be used to quantify proteins. As a result, MRM analysis is a popular alternative for biomarker identification and quantification. As the name implies, many MRMs may be monitored per study, allowing numerous substances to be detected in the same experiment.

## Slide 5: What is the sensitivity of MRM?
This is a very delicate procedure. It is feasible to detect peptide molecules that would ordinarily be missed by traditional MS methods. Peptides, for example, may be precisely quantified down to the femtomole level. Peptides can be quantified at a g/ml concentration in complicated samples like plasma.

## Slide 6: Is MRM appropriate for both absolute and relative quantification?
This method can get results for any form of quantification. Although relative quantitation is very simple, absolute quantitation necessitates the use of proper standards. To get a measure of protein concentration, a particular peptide is quantitated against a spiking internal standard (e.g., a synthetic stable isotope labelled peptide standard).

## Slide 7: Is it necessary to design a method?
Yes. Each project is unique, and developing and running the MRM analysis takes a significant amount of operator time. With sufficient chromatographic separation, some sample cleaning may be necessary for complicated combinations. Extra preparatory work is necessary for plasma and serum, and additional expenses will be charged.

## Slide 8: Team members
يوسف خليفة احمد
احمد فرغلي
ايهاب راشد مسعود
عبد الرحمن ماهر
ايه حسنى سعيد